DATEPRD: Date of the production record (format: dd/mm/yy).
WELL_BORE_CODE: A unique code identifying the wellbore.
NPD_WELL_BORE_CODE: A unique code assigned by the Norwegian Petroleum Directorate (NPD) for the wellbore.
NPD_WELL_BORE_NAME: The name of the wellbore as assigned by NPD.
NPD_FIELD_CODE: A unique code assigned by NPD for the field.
NPD_FIELD_NAME: The name of the field (in this case, "VOLVE").
NPD_FACILITY_CODE: A unique code assigned by NPD for the facility.
NPD_FACILITY_NAME: The name of the facility (e.g., "MÆRSK INSPIRER").
ON_STREAM_HRS: Number of hours the well was on stream (producing) during the reported day.
AVG_DOWNHOLE_PRESSURE: Average downhole pressure measured in the well during the reported day.
AVG_DOWNHOLE_TEMPERATURE: Average downhole temperature measured in the well during the reported day.
AVG_DP_TUBING: Average differential pressure in the tubing during the reported day.
AVG_ANNULUS_PRESS: Average pressure in the annulus (the space between the tubing and the casing) during the reported day.
AVG_CHOKE_SIZE_P: Average choke size percentage (this might represent the opening size of the choke as a percentage).
AVG_CHOKE_UOM: Unit of measure for the average choke size (percentage, %).
AVG_WHP_P: Average wellhead pressure during the reported day.
AVG_WHT_P: Average wellhead temperature during the reported day.
DP_CHOKE_SIZE: Differential pressure across the choke.
BORE_OIL_VOL: Volume of oil produced from the well during the reported day.
BORE_GAS_VOL: Volume of gas produced from the well during the reported day.
BORE_WAT_VOL: Volume of water produced from the well during the reported day.
BORE_WI_VOL: Volume of water injected into the well during the reported day.
FLOW_KIND: Type of flow (e.g., "production").
WELL_TYPE: Type of well (e.g., "WI" for water injection, "OP" for oil production).